## Slide 1: Hybrid-NL2SVA: Integrating RAG and Finetuning for LLM-based NL2SVA
Weihua Xiao, Derek Ekberg, Siddharth Garg, Ramesh Karri
25 Sep, 2025

## Slide 2: Outline
Introduction
Methodology
Experimental Results
Conclusion

## Slide 3: SystemVerilog Assertion (SVA)
Assertion used for verification
always_ff @(posedge clk) begin
if (!rst_n) begin
d1 <= 1'b0;
d2 <= 1'b0;
grant <= 1'b0;
end else begin
d1 <= req;
d2 <= d1;
grant <= d2;
end
end
Verilog code
Specification Document
Design Property
If req is 1 now, grant must be high exactly 2 cycles later.
Natural Language to SVA (NL2SVA)
SVA
assert property(
@(posedge clk)
disable iff (!rst_n)
req |->##2 grant
);
Verification

## Slide 4: Related Works of NL2SVA: Rule-based
When req rises and holds high for 2 cycles, then grant must be 1 on the 3rd cycle.
Natural Language Pattern | SVA Template
… | …
When <signal1> rises, then <signal2> must be high <N> cycles later. | assert property (@(posedge clk) $rose(<signal1>) ¦-> ##<N> <signal2>);
… | …
Rule-based Template
Best Matching
assert property(
@(posedge clk)
$rose(req) |-> ##3 grant
);
assert property(
@(posedge clk)
$rose(req) ##1 req[*2] |-> grant);
Golden SVA
Generated SVA
Need substantial manual effort
Miss hold condition
Wrong timing condition
Limitation of Rule-based Template

## Slide 5: Related Works of NL2SVA: LLM-based
When req rises and holds high for 2 cycles, then grant must be 1 on the 3rd cycle.
assert property(
@(posedge clk)
$rose(req) ##1 req ##1 req |=> grant);
assert property(
@(posedge clk)
$rose(req) ##1 req[*2] |-> ##3 grant);
Golden SVA
Generated SVA
Wrong use of |->, |=>
Lack of SVA knowledge!

## Slide 6: Hybrid-NL2SVA: Summary & Contribution
RAG Augmenting SVA Knowledge for LLM
Customized RAG Framework:
  RAG Database: Textbooks for Hardware Design & Verification
  Hybrid Retrieval + SVA Operator Rechecking
Synthetic Finetuning Dataset:
  Golden SVA + Prompt-guided Explanation
  Finetuned Qwen2.5-Coder-7B
Evaluation Dataset for NL2SVA

## Slide 7: Outline
Introduction
Methodology
Experimental Results
Conclusion

## Slide 8: Customized RAG Framework: Overall Flow
Proposed: Code Database + Hybrid Retrieval + Operator-based Rechecking

## Slide 9: Customized RAG Framework: Database Construction
…
10 Hardware Design & Verification Textbooks
Code Block
code-centric chunk
Code database

## Slide 10: Customized RAG Framework: Hybrid-Retrieval
Retrieval Path 2
Retrieval Path 1

## Slide 11: Customized RAG Framework: Rechecking

## Slide 12: Synthetic Fine-tuning Dataset
Four layers of an example concurrent assertion.
SVA Construction: Layer-by-Layer

## Slide 13: Synthetic Fine-tuning Dataset
for every rising edge of the clock pclk at which a given reference signal refSig is true, the stable-value check on another signal StableSig succeeds in that same cycle.
assert property(
@(posedge pclk)
refSig |-> $stable(StableSig));

## Slide 14: Evaluation Dataset
40 Designs
229 Concurrent Assertions + Human-generated Explanations
Number of SVA operators and signals in the 229 SVAs.

## Slide 15: Outline
Introduction
Methodology
Experimental Results
Conclusion

## Slide 16: Experimental Setup
Evaluation Metric:
  Syntax Correct (SC)
  Functionality Match (FM)
Verification Tool: Cadence JasperGold
Evaluate Customized RAG Framework:
  RAG Database: 10 hardware design and verification textbooks
  LLMs: DeepSeek v3, OpenAI gpt-4o-mini, CodeX,

## Slide 17: Evaluation Results: Dynamic Splitting

## Slide 18: Evaluation Results: Hybrid Retrieval

## Slide 19: Evaluation Results: Customized RAG Framework

## Slide 20: Experimental Setup
Finetuning LLM: Qwen2.5-Coder-7B-Instruct
Finetuning Dataset: 4070 datapoints
  Golden SVA
  Natural Language Explanation
  Prompt-guided Explanation
Finetuning Framework: Llama-Factory [1]
8 A100 GPUs, ~2 hours

## Slide 21: Evaluation Results: Finetuned LLM

## Slide 22: Outline
Introduction
Methodology
Experimental Results
Conclusion

## Slide 23: Conclusion
Customized RAG framework for NL2SVA
  Dynamic Splitting + Hybrid Retrieval + Operator-based Rechecking
Synthetic fine-tuning dataset with prompt-guided explanations
  Layer-by-layer breakdown: Boolean → Sequence → Property → Verification
Largest NL2SVA evaluation dataset to date
  40 Verilog designs, 229 formally verified assertions with annotations
Evaluation across LLMs (GPT-4o-mini, CodeX, DeepSeek-V3, fine-tuned Qwen2.5-Coder-7B)

## Slide 24: Thank you!