## Slide 1: LLMs for Bug Detection – Security Assertions
Rahul Kande, Vasudev Gohil, Matthew DeLorenzo
Advisor: Prof. JV Rajendran
Texas A&M University

## Slide 2: Massive Growth in HW Vulnerabilities
Hardware vulnerabilities emerging at an alarming rate
Chart: 
| 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
Series 1 | 2 | 2 | 3 | 1 | 5 | 5 | 13 | 7 | 8 | 6 | 1 | 3 | 8 | 16 | 6 | 17 | 36 | 33 | 48 | 41 | 58 | 92
Total documented hardware vulnerabilities (CVEs) by year
Source: National Vulnerability Database
How to detect vulnerabilities at the pre-silicon stage?
Assertion-based Verification
Notes: As hardware designs continue to increase in size and complexity over recent years, in part due to the trend of Moores law, this also results in a large increase in hardware vulnerabilities, in which design flaws by hardware engineers can be exploited by potential malicious attackers. This increase in hardware vulnerabilities is shown in the graph above, demonstrating a steep rise in hardware CVEs, or common vulnerabilities and exposures, over the past few years in particular. This is particularly concerning as hardware vulnerabilities often can not be easily patched like a software bug. Furthermore, if the underlying hardware is not secure, software programs that run on top can also vulnerable to malfunction, even if the software is completely secure on its own. Our hardware is assumed to be a root of trust in development and utilization, and should therefore be free of these vulnerabilities.
Therefore, hardware designers need methodologies to detect these vulenrabilities before the hardware is manufactured, or in the pre-silicon stage. One such way to accomplish this is a design strategy called assertion-based verification.

## Slide 3: Hardware Assertions
Statements about a circuit design expected to be always be true.
  SystemVerilog Assertions (SVA)
Critical component in hardware verification.
  Verify individual functional properties, critical logic.
Detects vulnerabilities early in the design process.
Two types: immediate, and concurrent verifications.
Notes: Hardware assertions can be defined as statements about a circuits design, or intended functionality, that are always expected to be true.
These statements can be utilized in programming languages for hardware design at the register level, such as SystemVerilog assertions.
These statements are meant to verify critical components with hardware verificatio, including individual functions and critical logic in the desing.
Through these statemetns, we are able to detect vulnerabilities early in the design process, enabling engineers to address them before manufacture.
When considering hardware assertions, there are two main types that are utilized, including immeadiate and concurrent verificaitons.

## Slide 4: Immediate Assertions
If-statement.
Not dependent on clock/reset signals.
Ex: Ensure that the current_state is never 0.
immediate_assertion_name:
assert (current_state != 0)
else
error message $error("%m checker failed");
Notes: Immeadate assertions can be thought of as simple if-statements as in programming, as these assertions are not dependent on clock or reset signals.
An example of this is shown above in which a designs state should never be qual to 0.
In this case we can create an dassertions that checks if the state is 0, and throws an error if the state is true.

## Slide 5: Concurrent Assertions
More complex statements.
Span time, triggered relative to the clock edge.
  Keyword “property”.
Ex: Check that an ack signal arrives 3-5 clock cycles after a request.
assert property (@(posedge clk) req |-> ##[3:5] ack);

## Slide 6: Hardware Vulnerability Detection
RISC-V Hack@DAC SoC
Register Lock Security Feature “Locked data is not accessible”
module rsa_wrapper(
input clk,
input rst_ni,
input reglk,
input debug_req,
input jtag_unlock,
input [31:0] address,
input we,
input [31:0] wdata,
output [31:0] rdata
);
. . .
assign debug_en =
debug_reg & jtag_unlock;
assign read_en = (!reglk) || debug_en;
. . .
// Implement MD5 I/O memory map interface
// Read side
always @(clk) begin
if (!rst_ni)
. . .
else if(!we) begin
case(address[10:3])
0:
rdata <= read_en ? msg: 0;
. . .
default:
;
endcase // address[10:3]
end
end
. . .
endmodule

## Slide 7: Hardware Vulnerability Detection
RISC-V Hack@DAC SoC
Register Lock Security Feature “Locked data is not accessible”
Buggy Verilog Implementation
module rsa_wrapper(
input clk,
input rst_ni,
input reglk,
input debug_req,
input jtag_unlock,
input [31:0] address,
input we,
input [31:0] wdata,
output [31:0] rdata
);
. . .
assign debug_en =
debug_reg || jtag_unlock;
assign read_en = (!reglk) || debug_en;
. . .
// Implement MD5 I/O memory map interface
// Read side
always @(clk) begin
if (!rst_ni)
. . .
else if(!we) begin
case(address[10:3])
0:
rdata <= read_en ? msg: 0;
. . .
default:
;
endcase // address[10:3]
end
end
. . .
endmodule

## Slide 8: Hardware Vulnerability Detection
RISC-V Hack@DAC SoC
Register Lock Security Feature “Locked data is not accessible”
Buggy Verilog Implementation
module rsa_wrapper(
input clk,
input rst_ni,
input reglk,
input debug_req,
input jtag_unlock,
input [31:0] address,
input we,
input [31:0] wdata,
output [31:0] rdata
);
. . .
assign debug_en =
debug_reg || jtag_unlock;
assign read_en = (!reglk) || debug_en;
. . .
// Implement MD5 I/O memory map interface
// Read side
always @(clk) begin
if (!rst_ni)
. . .
else if(!we) begin
case(address[10:3])
0:
rdata <= read_en ? msg: 0;
. . .
default:
;
endcase // address[10:3]
end
end
. . .
endmodule
Hardware assertions
assert property (@(posedge clk) disable iff ((!rst_ni))
(rdata != 0) |-> ($past(reglk) == 0) || ($past(jtag_unlock) == 1))
else $display("ERROR, Register access violated!!, time=%4d", $time);
Signal names
Conditions
Timing
Signal values
Signal values
Constraints
Syntax
Can we automate assertion generation?

## Slide 9: Limitations of Assertion-based Verification
Tedious manual effort
Error-prone
Scalability issues

## Slide 10: (Security) Assertions by Large Language Models
R. Kande et al.
Published at IEEE TIFS 2024
Notes: Prompts with varying level of detail and complexity automatically generated based on various codes and clues for the assertion/
From here the assertion file for a myriad of circuit designs is processed and altered through syntax correction tools, and simulated.

## Slide 11: LLMs for Hardware Vulnerability Detection
(Security) Assertions by Large Language Models, TIFS 2024
LLM evaluation framework
10 Benchmarks HW CWEs
7 Prompt Evaluation Metrics
2K+ Prompt Configurations
200K+ Assertions Generated
Chart: Accuracy of Different Prompt Configurations
| 0 | 500 | 1000 | 1500 | 2000
Column1
93.55% accuracy
0% accuracy
Accuracy varies extremely with prompts
Notes: More detail – more success
- Still need an amount fo security expertise

## Slide 12: Demo
https://colab.research.google.com/drive/1OG5nmWKTvbsvfmMrlIy3L-0U1wzWOtkS?usp=sharing
Notes: assert property (@(posedge clk) (signal == GREEN) |-> ($past(signal) == RED));

## Slide 13: Tutorial Task – New Bug Diagram
Notes: assert property (@(posedge clk) (signal == GREEN) |-> ($past(signal) == RED));

## Slide 14: Tutorial Task – Solution Example
#@title Finding the bug - Solution
prompt = "Complete the following hardware assertion to check that at \
every positive edge of clk, if the value of the signal register is GREEN, then \
the value of the signal register in the previous clock cycle is RED\nassert property. "
prompt += "An example of hardware assertion to check that at every \
positive edge of clock, if the value of the data register is DONE, \
then the value of the data register in the previous clock cycle is either VALID\
or DONE is: assert property (@(posedge clk) (data == DONE) |-> ($past(data) == VALID) || ($past(data) == DONE));"
model = ChatGPT3p5() # <-- we are using ChatGPT 3.5
messages=[ # <-- this is the prompt to LLM
{"role": "system", "content": "You are a helpful assistant."},
{"role": "user", "content": prompt}
]
print(model.generate(messages)) # <-- this prints the response from the LLM
#print(model.generate(messages,seed=12345,temperature=0.0)) # <-- this tries to generate a deterministic response from the LLM
#check for something thats valid
#- transitions into red should happen through yellow or red.
#- similar - transitions into green - happen through red or green.
#- Check reset behavior -
#assert property (@(posedge clk) (signal == GREEN) |-> ($past(signal) == RED));
Notes: assert property (@(posedge clk) (signal == GREEN) |-> ($past(signal) == RED));

## Slide 15
Thank You
Matthew DeLorenzo
Secure and Trustworthy Hardware (SETH) Lab
https://seth.engr.tamu.edu
Texas A&M University
(Security) Assertions by Large Language Models

## Slide 16: Conclusion

## Slide 18: LLM Generation Process
The
sky
is
Token | Probability
blue | 38%
clear | 20%
usually | 8%
the | 3%
… | 
More likely ↑
Less likely ↓
blue

## Slide 19: LLMs for Chip Design
Iterative Chip Design
⎯⎯⎯⎯⎯⎯
⎯⎯⎯⎯⎯⎯
⎯⎯⎯⎯⎯⎯
LLM
always @(posedge clk)
. . .
always @(posedge clk)
. . .
Verilog Generation
Finding Bugs

## Slide 20: Ongoing and Future Work
On Hardware Security Bug Code Fixes By Prompting Large Language Models
Fixing Hardware Security Bugs with Large Language Models
FLAG: Finding Line Anomalies (in code) with Generative AI
Make Every Move Count: LLM-based High-Quality RTL Code Generation Using MCTS
always @(posedge clk)
. . .

## Slide 21: Resources
Tutorial GitHub link: https://github.com/JBlocklove/LLMs-for-EDA-Tutorial/tree/main
Generating HDL with Feedback Loops
  Colab: https://colab.research.google.com/drive/1Va3Jp5zwr4RW-zrCHIHQvJ8pmhN-EFpD?usp=sharing
  Slides: https://docs.google.com/presentation/d/11LRoS_cXT9edCsGC3phwMg8PaxwQasIfkjv0TKSbjOY/edit?usp=sharing
VeriGen
  Colab: https://colab.research.google.com/drive/1ej8KTGtwqz3k4ZKDTeprmhELZinbEIdQ?usp=sharing
  Slides: https://docs.google.com/presentation/d/1YkYKaaPcDMpd8W5t-eU0Ay_4NxClxU_J5_VSo-iDZ10/edit?usp=sharing
LLM for Bug Detection
  Colab: https://colab.research.google.com/drive/1NJKfDE5GxWru92vUK4k-kVncMK3Znufx?usp=sharing
  Slides: https://tamucs-my.sharepoint.com/:p:/g/personal/gohil_vasudev_tamu_edu/EZLbyLfKxoZGk7YHE5QNPrUB_TlHbohVJ_FvL_GI__oLmw?e=Rpv4Wz

## Slide 22: Hardware Design
Hardware (root-of-trust)
Register-Transfer-Level (RTL)
Hardware description languages (HDLs)
  Verilog, SystemVerilog, VHDL
Thousands of RTL code lines
Synthesized into registers, wires and hardware logic
Is this RTL secure?

## Slide 23: LLM Training Process
Synthetic Data (e.g., Cosmopedia)
Pre-Trained LLM
Training
The
sun
rises
in
the
east
Token/word sequence seen so far
Predicted token

## Slide 24: LLM Generation Process
The
sky
is
Token | Probability
blue | 38%
clear | 20%
usually | 8%
the | 3%
… | 
More likely ↑
Less likely ↓
blue

## Slide 25: LLMs for Chip Design
Verilog Generation
⎯⎯⎯⎯⎯⎯
⎯⎯⎯⎯⎯⎯
⎯⎯⎯⎯⎯⎯
LLM
Conversational Chip Design
always @(posedge clk)
. . .
always @(posedge clk)
. . .
Fixing Security Bugs
define_design_lib . . .
set link_library . . .
. . .
EDA Script Generation